## Slide 1: CMSC 411 Performance (Cont…), Benchmarks, and Performance Pitfalls
Ergun Simsek
Fall 2022 - Lecture 3

## Slide 2: Last Week
Compiler
Assembler
Tunnel

## Slide 3: Instruction Count and CPI
Instruction Count for a program
  Determined by
    Program
    Instruction set architecture (ISA)
    Compiler
Average cycles per instruction (“CPI”)
  Determined by CPU hardware
  If different instructions have different CPI
    Average CPI affected by instruction mix
Last week, we said that we always want to improve the performance

## Slide 4: Program Clock Cycles
Instead of reporting execution time in seconds, we often use clock cycle counts
  Why? A newer generation of the same processor…
    Often has the same cycle counts for the same program
    But often has different clock speed (ex, 1 GHz changes to 1.5 GHz)

## Slide 5: Instruction Count and CPI
Some operations (e.g., division) require longer time to execute
Longer time = A higher number of cycles
CPI: Average number of cycles per instruction

## Slide 6: CPI Examples
PDP-11, VAX, Intel 8086: CPI > 1
Load/Store RISC machines CPI = 1
  MIPS, SPARC, PowerPC, miniMIPS
Modern CPUs CPI < 1
  Pentium4 0.33
  Xeon 0.25
  M2 ?

## Slide 7: How to Improve Performance?
Many ways to write the same equations:
So, to improve performance (everything else being equal) you can either
  ________ the # of required cycles for a program;
  ________ the clock cycle time or, said another way,
  ________ the clock rate;
  ________ the CPI (average clocks per instruction).
Decrease
Decrease
Increase
Decrease

## Slide 8: Example
Our favorite program runs in 10 seconds on computer A, which has a 2 GHz clock.
We are trying to help a computer designer build a new machine B, to run this program in 6 seconds.
The designer can use new (or perhaps more expensive) technology to substantially increase the clock rate, but has informed us that this increase will affect the rest of the CPU design, causing machine B to require 1.2 times as many clock cycles as machine A for the same program.
What clock rate should we tell the designer to target?
Computer A runs the code using 10*2e9 cycles.
Computer B will require 1.2 times more, so it will use 1.2* 10*2e9 cycles.
1.2* 10*2e9 = 6 * frequency_of_the_new_CPU  it has t be 4 GHz

## Slide 9: Now that we understand cycles
A given program will require
  some number of instructions (machine instructions)
  some number of cycles
  some number of seconds
We have a vocabulary that relates these quantities:
  cycle time (seconds per cycle)
  clock rate (cycles per second)
  CPI (average clocks per instruction)
    a floating point intensive application might have a higher CPI

## Slide 10: Performance Traps
Performance is determined by the execution time of a program that you care about.
Do any of the other variables equal performance?
  # of cycles to execute program?
  # of instructions in program?
  # of cycles per second?
  average # of cycles per instruction?
  average # of instructions per second?
Common pitfall:
  Thinking that only one of the variables is indicative of performance when it really is not!

## Slide 11: CPI Example
Suppose we have two implementations of the same instruction set architecture (ISA) on two computers and we are running the same program:
    Computer A has a clock cycle time of 250 ps and a CPI of 2.0
    Computer B has a clock cycle time of 500 ps and a CPI of 1.2
Which quantity (e.g., clock rate, CPI) is the same for two implementations?
What machine is faster for this program, and by how much?
A is faster by 1.2 X
Instruction Count

## Slide 12: CPI in More Detail
If different instruction classes take different numbers of cycles
Weighted average CPI:
Relative frequency

## Slide 13: Example: Compiler’s Impact
Two different compilers are being tested for a 500 MHz machine with three different classes of instructions: Class A, Class B, and Class C, which require 1, 2, and 3 cycles (respectively).
Both compilers are used to produce code for a large piece of software.
The first compiler's code uses 5 million Class A instructions, 1 million Class B instructions, and 2 million Class C instructions.
The second compiler's code uses 7 million Class A instructions, 1 million Class B instructions, and 1 million Class C instructions.
Which program uses fewer instructions?
  Instructions1 = (5+1+2) x 106 = 8 x 106
  Instructions2 = (7+1+1) x 106 = 9 x 106
Which sequence uses fewer clock cycles?
  Cycles1 = (5(1)+1(2)+2(3)) x 106 = 13 x 106
  Cycles2 = (7(1)+1(2)+1(3)) x 106 = 12 x 106
CPI1 = ?
13/8 = 1.625
CPI2 = ?
12/9 = 1.33

## Slide 14: CPI Example
Alternative compiled code versions using instructions in classes A, B, C. Which version has a lower CPI?
Version 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Class | A | B | C
CPI for class | 1 | 2 | 3
IC for version 1 | 2 | 1 | 2
IC for version 2 | 4 | 1 | 1
Version 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5

## Slide 15: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Cycle Time
The BIG Picture

## Slide 16: Benchmarks
Performance best determined by running a real application
  Use programs typical of expected workload
  Or, typical of expected class of applications
    e.g., compilers/editors, scientific applications, graphics, etc.
Small benchmarks
  nice for architects and designers
  easy to standardize
  can be abused
SPEC (System Performance Evaluation Cooperative)
  companies have agreed on a set of real program and inputs
  can still be abused
  valuable indicator of performance (and compiler technology)
https://www.spec.org/

## Slide 17: SPEC 2017
Integers
Floating Point
Kilo Lines of Code
throughput
time

## Slide 18: Other Popular Benchmarks
Several others popular
  industry uses SPEC
  but ordinary consumers use others
    more representative of the work they do!
      e.g., gaming, Photoshop/Aperture, copying huge files, multimedia coding/decoding, etc.
    Geekbench is quite popular!

## Slide 19: Fallacies and pitfalls
The improvement of one aspect of a computer to increase overall performance by an amount proportional to the size of the improvement.
Computers at low utilization use little power
Designing for performance and designing for energy efficiency are unrelated goals
Using a subset of the performance equation is a better performance metric
W
R
O
N
G

## Slide 20: Amdahl’s Law
Possibly the most important law regarding computer performance:
  Principle: Make the common case fast!
  Eventually, performance gains will be limited by what cannot be improved
    e.g., you can raise the highway speed limit, but the city speed limit stays the same
Gene Amdahl (1973)
Notes: gives the theoretical speedup in latency of the execution of a task at fixed workload that can be expected of a system whose resources are improved.

## Slide 21: Amdahl’s Law: Example
Suppose a program runs in 100 seconds on a machine, where multiplies are executed 80% of the time.
How much do we need to improve the speed of multiplication if we want the program to run 4 times faster?
How about making it 5 times faster?
25 = 80/r + 20 r = 16x
20 = 80/r + 20 r = ?

## Slide 22: Example
Suppose we enhance a machine making all floating-point instructions run FIVE times faster.
If the execution time of some benchmark before the floating-point enhancement is 10 seconds, what will the speedup be if only half of the 10 seconds is spent executing floating-point instructions?
We are looking for a benchmark to show off the new floating-point unit described above, and want the overall benchmark to show at least a speedup of 3.
What percentage of the execution time would floating-point instructions have to account for in this program in order to yield our desired speedup on this benchmark?
5/5 + 5 = 6 Relative Perf = 10/6 = 1.67 x
10/3 = f/5 + (10 – f) = 10 – 4f/5 f = 83.33

## Slide 23: Power Consumption
Power = Energy consumed per unit time
Two contributors to power consumption
  Dynamic power
    power consumed when doing actual work
    called dynamic because components and wires are switching between ‘0’ and ‘1’
  Static or ‘leakage’ power
    power consumed even when everything is idle or ‘static’
    due to some small amount of ‘leakage’ current that still flows

## Slide 24: Dynamic Power Consumption
Energy consumed due to switching activity:
  All wires and transistor gates have capacitance
  Energy required to charge a capacitance, C, to VDD is CVDD2
  Circuit running at frequency f: transistors switch (from 1 to 0 or vice versa) at that frequency
  Capacitor is charged 0.5f times per second
    Pdynamic = ½CVDD2f
C is the total capacitance of circuit (“capacitive load”)
VDD is the supply voltage
f is the switching frequency

## Slide 25: Static Power Consumption
Power consumed when no gates are switching
  Caused by the quiescent supply current, IDD (also called the leakage current)
Pstatic or Pleakage = IDDVDD
VDD is the supply voltage
IDD is the leakage current

## Slide 26: Power Consumption Example
Estimate the power consumption of a wireless handheld computer
  VDD = 1.2 V
  C = 20 nF
  f = 1 GHz
  IDD = 20 mA
P = ½CVDD2f + IDDVDD
= ½(20 nF)(1.2 V)2(1 GHz) + (20 mA)(1.2 V)
= 14.4 W + 24 mW
= 14.424 W

## Slide 27: Power Trends
In CMOS IC technology
×1000
×30
5V → 1V
Notes: Both clock rate and power increased rapidly for decades, and then flattened off recently. The reason they grew together is that they are correlated, and the reason for their recent slowing is that we have run into the practical power limit for cooling commodity microprocessors.
With Pentium 4, Intel was aiming to reach clock rate of 10 GHz!

## Slide 28: Reducing Power
How power reduction is achieved if we replace the old CPU wit a new one which has
  85% of capacitive load of old CPU
  15% voltage and 15% frequency reduction
The power wall
  We cannot reduce voltage further
Threshold Voltage
near Leakage Limit

## Slide 29: Moore’s Law: Uniprocessor Perf.
Constrained by power, instruction-level parallelism, memory latency

## Slide 30: Fallacies and pitfalls
The improvement of one aspect of a computer to increase overall performance by an amount proportional to the size of the improvement.
Computers at low utilization use little power
Designing for performance and designing for energy efficiency are unrelated goals
Using a subset of the performance equation is a better performance metric
W
R
O
N
G

## Slide 31: Fallacy: Low Power at Idle
AMD X4 power benchmark:
  At 100% load: 295W (max power)
  At 50% load: 246W (83% max power)
  At 10% load: 180W (still consumes 61% of max power)
Google data center
  Mostly operates at 10% - 50% load
  At 100% load less than 1% of the time
Industry challenge: Design processors to make power proportional to load

## Slide 32: Fallacies and pitfalls
The improvement of one aspect of a computer to increase overall performance by an amount proportional to the size of the improvement.
Computers at low utilization use little power
Designing for performance and designing for energy efficiency are unrelated goals
Using a subset of the performance equation is a better performance metric
W
R
O
N
G

## Slide 33: Multiprocessors
“Multicore” microprocessors
  More than one processor core per chip
Requires explicitly parallel programming
  Hardware executes multiple instructions at once
    Ideally, hidden from the programmer
  Hard to do
    Programming for performance
    Load balancing
    Optimizing communication and synchronization
    But, newer OSs and libraries have been designed for this

## Slide 34: Fallacies and pitfalls
The improvement of one aspect of a computer to increase overall performance by an amount proportional to the size of the improvement.
Computers at low utilization use little power
Designing for performance and designing for energy efficiency are unrelated goals
Using a subset of the performance equation is a better performance metric
W
R
O
N
G

## Slide 35: A Useless Computer Performance Measure: MIPS
Millions of Instructions per Second
Frequency in MHz
CPI (Average Clocks Per Instruction)
Unfortunate coincidence:
This “MIPS” has nothing to do with the name of the MIPS processor we will be studying!
Pitfall: Cannot compare MIPS of two different processors if they run different sets of instructions!
 Meaningless Indicator of Processor Speed!

## Slide 36: Remember
Performance is specific to a particular program
  Total execution time is a consistent summary of performance
For a given architecture, the performance comes from:
  increases in clock rate (without adverse CPI affects)
  improvements in processor organization that lower CPI
  compiler enhancements that lower CPI and/or instruction count
Improvements in one aspect of a machine’s performance do not bring linear improvement in the total performance
Power is a limiting factor
  Use parallelism to improve performance