## Slide 1: CMSC 411 Lecture 4: Representing Operands
Ergun Simsek
Characters
Integers
  Positive numbers
  Negative numbers
Non-Integers
  Fixed-Point Numbers
  Floating-Point Numbers

## Slide 2: Motivation
Computer use binary representation internally
  a wire is “hot” or “cold”
  a switch is “on” or “off”
How do we use bits to represent information?
We need standards of representations for
  Letters and Numbers
  Colors/pixels
  Music and video
  …

## Slide 3: Information Encoding
Encoding = assign representation to information
Examples:
  suppose you have two “things” (symbols) to encode
    one is  and other 
    what would you do?
  now suppose you have 4 symbols to encode
    h, d, b and z
  now suppose you have the following numbers to encode
    1, 3, 5 and 7
What about
Quantum Computing!!!

## Slide 4: Encoding is an art
Choosing an appropriate and efficient encoding is a real engineering challenge (and an art)
Impacts design at many levels
  Complexity (how hard to encode/decode)
  Efficiency (#bits used, transmit energy)
  Reliability (what happens with noise?)
  Security (encryption)

## Slide 5: Fixed-Length Encodings
What is fixed-length encoding?
  All symbols are encoded using the same number of bits
When to use it?
  If all symbols are equally likely (or we have no reason to expect otherwise)
When not to use it?
  When some symbols are more likely, while some are rare
  What to use then: Variable-length encoding
  Example:
    Suppose probabilities using an getting an X, Y, or Z are 55%, 30%,and 15%
    How would we encode them?

## Slide 6: Fixed-Length Encodings
Length of a fixed-length code
  use as many bits as needed to unambiguously represent all symbols
    1 bit suffices for 2 symbols
    2 bits suffice for …?
    n bits suffice for …?
    how many bits needed for M symbols?
  ex. Decimal digits 10 = {0,1,2,3,4,5,6,7,8,9}
    4-bit binary code: 0000 to 1001
  ex. ~84 English characters = {A-Z (26), a-z (26), 0-9 (10), punctuation (8), math (9), financial (5)}
    7-bit ASCII (American Standard Code for Information Interchange)
ceil

## Slide 7: Encoding Characters
ASCII Code: use 7 bits to encode 128 characters

## Slide 8: Encoding More Characters
ASCII is biased towards western languages, esp. English
In fact, many more than 256 chars in common use: â, ğ, ö, ñ, è, ¥, 揗, 敇, 횝, カ, ℵ, ℷ, ж, ค
Unicode is a worldwide standard that supports all languages, special characters, classic, and arcane
  Several encoding variants, e.g. 16-bit (UTF-8)
0
x
x
x
x
x
x
x
ASCII equiv range:
1
0
x
x
x
x
x
x
1
1
0
y
y
y
y
x
16-bit Unicode
1
0
x
x
x
x
x
x
1
0
z
y
y
y
y
x
1
1
1
0
z
z
z
z
24-bit Unicode
1
0
x
x
x
x
x
x
1
0
z
y
y
y
y
x
1
1
1
1
0
w
w
w
1
0
w
w
z
z
z
z
32-bit Unicode

## Slide 9: Encoding Positive Integers
How to encode positive numbers in binary?
  Each number is a sequence of 0s and 1s
  Each bit is assigned a weight
  Weights are increasing powers of 2, right to left
  The value of an n-bit number is
211
210
29
28
27
26
25
24
23
22
21
20
0
1
1
1
1
1
0
1
0
0
0
0
24 = 16
+ 28 = 256
+ 26 = 64
+ 27 = 128
+ 29 = 512
+ 210 = 1024
2000ten

## Slide 10: Some Bit Tricks
Memorize the first 10 powers of 2
2. Memorize the prefixes for powers of 2 that are multiples of 10
    20 = 1 25 = 32
    21 = 2 26 = 64
    22 = 4 27 = 128
    23 = 8 28 = 256
    24 = 16 29 = 512
  210 = Kilo (1024)
  220 = Mega (1024*1024)
  230 = Giga (1024*1024*1024)
  240 = Tera (1024*1024*1024*1024)
  250 = Peta (1024*1024*1024*1024*1024)
  260 = Exa (1024*1024*1024*1024*1024*1024)

## Slide 11: Some Bit Tricks (Cont…)
When you convert a binary number to decimal, first break it down into clusters of 10 bits.
Then compute the value of the leftmost remaining bits (1) find the appropriate prefix (e.g. above it should be GIGA) (why? Remember it is kilo, mega, giga, etc.)
Compute the value of and add in each remaining 10-bit cluster
0000101000
0000001100
0000000011
01

## Slide 12: Other Helpful Clusterings: Octal
Sometimes convenient to use other number “bases”
  often bases are powers of 2: e.g., 8, 16
    allows bits to be clustered into groups
  base 8 is called octal  groups of 3 bits
    Convention: lead the number with a 0
211
210
29
28
27
26
25
24
23
22
21
20
0
1
1
1
1
1
0
1
0
0
0
0
Octal - base 8
000 - 0 001 - 1 010 - 2 011 - 3 100 - 4 101 - 5 110 - 6 111 - 7
= 200010
0
2
7
3
200010
0*80 = 0
+ 3*83 = 1536
+ 2*81 = 16
+ 7*82 = 448
200010=037208

## Slide 13: One Last Clustering: HEX
Base 16 is most common!
  called hexadecimal or hex  groups of 4 bits
  hex ‘digits’ (“hexits”): 0-9, and A-F
  each hexit position represents a power of 16
    Convention: lead with 0x
211
210
29
28
27
26
25
24
23
22
21
20
0
1
1
1
1
1
0
1
0
0
0
0
Hexadecimal - base 16
0000 - 0 1000 - 8 0001 - 1 1001 - 9 0010 - 2 1010 - a 0011 - 3 1011 - b 0100 - 4 1100 - c 0101 - 5 1101 - d 0110 - 6 1110 - e 0111 - 7 1111 - f
= 200010
0
d
7
200010
0*160 = 0
+ 13*161 = 208
+ 7*162 = 1792
= 0x7d016

## Slide 14: Signed-Number Representations
What about signed numbers?
  one obvious idea: use an extra bit to encode the sign
    convention: the most significant bit (leftmost) is used for the sign
    called the SIGNED MAGNITUDE representation
S
210
29
28
27
26
25
24
23
22
21
20
0
1
1
1
1
1
0
1
0
0
0
0
2000
1
-2000

## Slide 15: Signed-Number Representations
The Good: Easy to negate, find absolute value
The Bad:
  add/subtract is complicated
    depends on the signs
    4 different cases!
  two different ways of representing a 0
  it is not used that frequently in practice
    except in floating-point numbers

## Slide 16: Alternative: 2’s Complement Rep.
20
21
22
23
…
2N-2
-2N-1
…
…
N bits
The 2’s complement representation for signed integers is the most commonly used signed-integer representation. It is a simple modification of unsigned integers where the most significant bit is considered negative.
sign bit
Range: – 2N-1 to 2N-1 – 1
8-bit 2’s complement example:
11010110 = –27 + 26 + 24 + 22 + 21
= – 128 + 64 + 16 + 4 + 2 = – 42
ladders
chute

## Slide 17: Why 2’s Complement?
Benefit: the same binary addition (mod 2n) procedure will work for adding positive and negative numbers
  Don’t need separate subtraction rules!
  The same procedure will also handle unsigned numbers!
  NOTE: We typically ignore the leftmost carry
Example:
5510 = 001101112
+ 1010 = 000010102
6510 = 010000012
5510 = 001101112
+ -1010 = 111101102
4510 = 1001011012
When using signed magnitude representations, adding a negative value really means to subtract a positive value. However, in 2’s complement, adding is adding regardless of sign. In fact, you NEVER need to subtract when you use a 2’s complement representation.

## Slide 18: 2’s Complement
How to negate a number?
  First complement every bit (i.e. 1  0, 0  1), then add 1
    4-bit example (Convert + number to a – and vice versa)
      +5 = 0101  -5 = 1010 + 1 = 1011 = 1+2-8
      -5 = 1011  +5 = 0100 + 1 = 0101 = 1+4
    8-bit example (Convert + number to a – and vice versa)
      +20 = 00010100  -20 = 11101011 + 1 = 11101100
      -20 = 11101100  +20 = 00010011 + 1 = 00010100
  Why does this work?
    Proof on board. Hint:
for bi = 1

## Slide 19: 2’s Complement
How to negate a number?
  Method:
    Complement every bit
    Add 1 to LSB
  Shortcut
    Keep the rightmost “1” and any following “0”s as they are
    Complement all remaining bits
    Example: 1001000  0111000

## Slide 20: 2’s Complement
Sign-Extension
  suppose you have an 8-bit number that needs to be “extended” to 16 bits
    Why? Maybe because we are adding it to a 16-bit number…
  Examples
    16-bit version of 42 = 0000 0000 0010 1010
    8-bit version of -2 = 1111 1110
  Why does this work?
    Same hint:
    Proof on board
1111 1111

## Slide 21: Tutorial on Base Conversion (+ve ints)
Binary to Decimal
  multiply each bit by its positional power of 2
  add them together
Decimal to Binary
  Problem: given v, find bi (inverse problem)
  Hint: expand series
    observe: every term is even except first
      this determines b0
      divide both sides by 2

## Slide 22: Tutorial on Base Conversion (+ve ints)
Decimal to Binary
  Problem: given v, find bi (inverse problem)
  Algorithm:
    Repeat
      divide v by 2
      remainder becomes the next bit, bi
      quotient becomes the next v
    Until v equals 0
Note: Same algorithm applies to other number bases
  just replace divide-by-2 by divide-by-n for base n

## Slide 23: Non-Integral Numbers
How about non-integers?
  examples
    1.234
    -567.34
    0.00001
    0.0000000000000012
  fixed-point representation
  floating-point representation

## Slide 24: Fixed-Point Representation
Set a definite position for the “binary” point
  everything to its left is the integral part of the number
  everything to its right is the fractional part of the number
  1101.0110 = 23 + 22 + 20 + 2-2 + 2-3
  = 8 + 4 + 1 + 0.25 + 0.125
  = 13.375
Or
1101.0110 = 214 * 2-4 = 214/16 = 13.375
23
22
21
20
2-1
2-2
2-3
2-4

## Slide 25: Fixed-Point Base Conversion
Binary to Decimal
  multiply each bit by its positional power of 2
  just that the powers of 2 are now negative
  for m fractional bits
Examples
  0.12 = ½ = 0.5ten
  0.00112 = 1/8 + 1/16 = 0.1875ten
  0.0011001100112= 1/8+1/16+1/128+1/256+1/2048+1/4096 = 0.19995117187ten (getting close to 0.2)
  0.00112 (repeats) = 0.2ten

## Slide 26: Fixed-Point Base Conversion
Decimal to Binary
  Problem: given v, find bi (inverse problem)
  Hint: this time, try multiplying by 2
    whole number part is b-1
    remaining fractional part is the rest
  Algorithm:
    Repeat
      multiply v by 2
      whole part becomes the next bit, bi
      remaining fractional part becomes the next v
    Until (v equals 0) or (desired accuracy is achieved)

## Slide 27: Repeated Binary Fractions
Not all fractions have a finite representation
  e.g., in decimal, 1/3 = 0.3333333… (unending)
In binary, many of the fractions you are used to have an infinite representation!
  Examples
    1/10 = 0.110 = 0.000110011…2=0.000112
    1/5 = 0.210 = 0.00112 = 0.333…16
Question
  In Decimal: When do fractions repeat?
    when the denominator is mutually prime w.r.t. 5 and 2
  In Binary: When do fractions repeat?
    when the denominator is mutually prime w.r.t. 2
    i.e., when denominator is anything other than a power of 2

## Slide 28: Signed fixed-point numbers
How do you incorporate a sign?
  use sign magnitude representation
    an extra bit (leftmost) stores the sign
    just as in negative integers
  2’s complement
    leftmost bit has a negative coefficient
    1101.0110 = -23 + 22 + 20 + 2-2 + 2-3
    = -8 + 4 + 1 + 0.25 + 0.125 = -2.625
    OR:
      first ignore the binary point, use 2’s complement, put the point back
    1101.0110 = (-128 + 64 + 16 + 4 + 2)* 2-4
    = -42/16 = -2.625
-23
22
21
20
2-1
2-2
2-3
2-4

## Slide 29: Signed fixed-point numbers
How to negate in 2’s complement representation
  Same idea: flip all the bits, and add “1” to the rightmost bit
    not the bit to the left of the binary point
  Example
    1101.0110 = -23 + 22 + 20 + 2-2 + 2-3
    = -8 + 4 + 1 + 0.25 + 0.125 = -2.625
    1101.0110  0010.1001 + 0.0001 = 0010.1010
    0010.1010 = 21 + 2-1 + 2-3
    = 2 + 0.5 + 0.125 = 2.625

## Slide 30: Bias Notation
Idea: add a large number to everything, to make everything look positive!
  must subtract this “bias” from every representation
  This representation is called “Bias Notation”.
1
1
0
1
0
1
1
0
20
25
24
23
22
21
26
27
Ex: (Bias = 127)
6 * 1 = 6
13 * 16 = 208
- 127
87
Why? Monotonicity

## Slide 31: Floating-Point Representation
Another way to represent numbers is to use a notation similar to Scientific Notation.
  This format can be used to represent numbers with fractions (3.90 x 10-4), very small numbers (1.60 x 10-19), and large numbers (6.02 x 1023).
  This notation uses two fields to represent each number. The first part represents a normalized fraction (called the significand), and the second part represents the exponent (i.e. the position of the “floating” binary point).
Normalized Fraction
“dynamic range”
“bits of accuracy”
Exponent

## Slide 32: IEEE 754 Floating-Point Formats
IEEE 754 Format
1 bit
S
1 bit
11 bits
S
52 bits
Significand
Exponent
23 bits
Significand
8 bits
Exponent
Single-precision format
Double-precision format

## Slide 33: IEEE 754 Single-precision Example

## Slide 34: In Closing
Selecting encoding scheme has imp. implications
  how this information can be processed
  how much space it requires.
Computer arithmetic is constrained by finite encoding
  Advantage: it allows for complement arithmetic
  Disadvantage: it allows for overflows, numbers too big or small to be represented
Bit patterns can be interpreted in an endless number of ways, however important standards do exist
  Two’s complement
  IEEE 754 floating point

## Slide 35: Next Class
  von Neumann model of a computer
  Instruction set architecture
  MIPS instruction formats
  Some MIPS instructions