## Slide 1: Introduction to Instruction Set Architecture
Ergun Simsek
Lecture 4

## Slide 2: Representing Instructions
Last class
  Representing Operands (Part 2)
    Integers
    Negative numbers
      Signed Magnitude Representation
      Two’s Complement Representation (How to negate)
    Non-integer numbers
      IEEE 754
Today
  von Neumann model of a computer
  Introduction to ISA (Instruction Set Architecture)

## Slide 3: A General-Purpose Computer
Most of today’s computers based on the model proposed by John von Neumann in the late 1940s
Major components of the von Neumann Model are:
Central
Processing Unit
Central Processing Unit (CPU): Fetches, interprets, and executes a specified set of operations called Instructions.
Main
Memory
Memory: storage of N words of W bits each, where W is a fixed architectural parameter, and N can be expanded to meet needs.
Input/
Output
I/O: Devices for communicating with the outside world.

## Slide 4: Open Questions in our Simple Model
We will answer the following questions today and in the following two lectures
  WHAT are INSTRUCTIONS?
  WHERE are INSTRUCTIONS stored?
  HOW are instructions represented?
  WHERE are VARIABLES stored?
  How are labels associated with particular instructions?
  How do you access more complicated variable types:
    Arrays?
    Structures?
    Objects?
  Where does a program start executing?
  How does it stop?

## Slide 5: Instructions and Programs
What are instructions?
  Words of a computer’s language
Instruction Set
  The full vocabulary
Stored Program Concept
  Instructions and data are stored in a common (memory) memory as numbers
Sequential semantics
  All instructions execute sequentially (or at least appear sequential to the programmer)
Note: MIPS is a family of reduced instruction set computer (RISC) instruction set architectures (ISA)
There is also CISC: Complex Instruction Set Computers

## Slide 6: Anatomy of an Instruction
An instruction is a primitive operation
  Instructions specify an operation and its operands (the necessary variables to perform the operation)
  Types of operands: immediate, source, and destination
add $t0, $t1, $t2
addi $t0, $t1, 1
Operation
Operands (variables, arguments, etc.)
Source Operands
Destination Operand
Immediate Operand
$X is a convention to denote the contents of a “register”, which is a location inside the CPU. In contrast, immediate operands indicate the value itself

## Slide 7: Meaning of an Instruction
Operations are abbreviated into opcodes (1-4 letters)
Instructions are specified with a very regular syntax
  First an opcode followed by arguments
  Usually (but not always) the destination is next, then source
  Why this order? Arbitrary…

## Slide 8: Being the Machine!
Instruction sequence
  Instructions are executed sequentially from a list …
    … unless some special instructions alter this flow
  Instructions execute one after another
    therefore, results of all previous instructions have been computed
$t0: 0
$t1: 6
$t2: 8
$t3: 10
Variables
add $t0, $t1, $t1
add $t0, $t0, $t0
add $t0, $t0, $t0
sub $t1, $t0, $t1
Instructions
12
24
48
42

## Slide 9: Anatomy of a von Neumann Computer
Control Unit
Data
Path
registers
MEMORY
control
status
instructions
data
PC
1101…1011
• INSTRUCTIONS coded in binary
• PROGRAM COUNTER or PC: Address of next instruction to be executed
• Control Unit has circuitry inside to translate instructions into control signals for data path
+4
R1 R2+R3
address
address
“Register File”
Register 0
Register 1
Register 31
32 bits

## Slide 10: The big picture: RISC
  Memory is distinct from data path
  Registers are in data path
  Program is stored in memory
  Control unit fetches instructions from memory
  Control unit tells data path what to do
  Data can be moved from memory to registers, or from registers to memory
  All data processing (e.g., arithmetic) takes place within the data path

## Slide 11
add $10, $11, $9
0
0
0
0
0
0
0
1
0
1
1
0
1
0
0
1
0
1
0
1
0
1
0
0
0
0
0
0
0
0
0
0
a =b + c

## Slide 12: MIPS Register Usage Conventions
Some MIPS registers assigned to specific uses
  by convention, so programmers can combine code pieces
    will cover the convention later
  $0 is hard-wired to the value 0

## Slide 13: Bit, Byte, and Word (in MIPS-lish)
Bit: 0 or 1 _
Byte: 8-bits _ _ _ _ _ _ _ _
Word: 32 bits = 4 bytes
_ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _
Little Endian vs Big Endian?
Every BYTE has a unique address = MIPS is a byte-addressable machine
Every instruction is one word

## Slide 14: MIPS Programming Model a representative simple RISC machine
Processor State (inside the CPU)
Fetch/Execute loop:
fetch Mem[PC]
PC = PC + 4†
execute fetched instruction (may change PC!)
repeat!
†MIPS uses byte memory addresses. However, each instruction is 32-bits wide, and *must* be aligned on a multiple of 4 (word) address. Each word contains four 8-bit bytes. Addresses of consecutive instructions (words) differ by 4.
00
PC
r0
r1
r2
...
r31
000000....0
32 bit “words”
General Registers:
A small scratchpad of frequently used or temporary variables
We’ll use a clean and sufficient subset of the MIPS-32 core Instruction set.
Main Memory
0
1
2
3
(4 bytes)
32 bit “words”
0
31
next instruction
0 4
8
16 20
Addresses

## Slide 15: Some MIPS Memory Nits
Memory locations are 32 bits wide
BUT, they are addressable in different-sized chunks
  8-bit chunks (bytes)
  16-bit chunks (shorts)
  32-bit chunks (words)
  64-bit chunks (longs/double)
We also frequently need access to individual bits! (Instructions help w/ this)
0
1
2
3
4
5
6
7
Addr
0:
4:
8:
12:
8
9
10
12
12
13
14
15
byte3 byte2 byte1 byte0
short2 short0
long0
long8
31 30 29 … … 4 3 2 1 0

## Slide 16: Programming a Processor
C code:
  f=(g+h)–(i+j);
Assembly:
  add t0,g,h
  add t1, i,j
  sub f, t0,t1
MIPS Assembly
  add R1, R4, R5
  add R2, R6, R7
  sub R3, R1, R2
Compiler
OS Loader
Memory
add R2, R6, R7
sub R3, R1, R2
0
4
8
12
16
20
24
28
32
add R1, R4, R5

## Slide 17: Execution of f=(g+h)-(i+j) in MIPS
Assume the following registers
R3=f
R4=g
R5=h
R6=I
R7=j
Control
Register File
0
f
g=2
h=3
R0
R1
R2
R3
R4
R5
R6
R7
R8
Memory
add R2, R6, R7
sub R3, R1, R2
0
4
8
12
16
20
24
28
32
Instruction Register
Program Counter
i=1
j=4
add R1, R4, R5
ALU

## Slide 18: Execution of f=(g+h)-(i+j) in MIPS
Assume the following registers
R3=f
R4=g
R5=h
R6=I
R7=j
Control
Register File
0
f
g=2
h=3
R0
R1
R2
R3
R4
R5
R6
R7
R8
Memory
add R2, R6, R7
sub R3, R1, R2
0
4
8
12
16
20
24
28
32
Instruction Register
Program Counter
0
i=1
j=4
add R1, R4, R5
ALU
0
add R1, R4, R5
add
5

## Slide 19: Execution of f=(g+h)-(i+j) in MIPS
Assume the following registers
R3=f
R4=g
R5=h
R6=I
R7=j
Control
Register File
0
f
g=2
h=3
R0
R1
R2
R3
R4
R5
R6
R7
R8
Memory
add R2, R6, R7
sub R3, R1, R2
0
4
8
12
16
20
24
28
32
Instruction Register
Program Counter
0
i=1
j=4
add R1, R4, R5
ALU
4
add
5
add R2, R6, R7
5

## Slide 20: Execution of f=(g+h)-(i+j) in MIPS
Assume the following registers
R3=f
R4=g
R5=h
R6=I
R7=j
Control
Register File
0
f
g=2
h=3
R0
R1
R2
R3
R4
R5
R6
R7
R8
Memory
add R2, R6, R7
sub R3, R1, R2
0
4
8
12
16
20
24
28
32
Instruction Register
Program Counter
4
i=1
j=4
add R1, R4, R5
ALU
8
sub
5
5
sub R3, R1, R2
0

## Slide 21: MIPS Register Nits
There are 32 named registers [$0, $1, …. $31]
The operands of all ALU instructions are registers
  This means to operate on a variables in memory you must:
    Load the value/values from memory into a register
    Perform the instruction
    Store the result back into memory
  Going to and from memory can be expensive
    (4x to 20x slower than operating on a register)
  Net effect: Keep variables in registers as much as possible!
Special purpose and conventions
  2 registers have specific “side-effects”
    (ex: $0 always contains the value ‘0’… more later)
  4 registers dedicated to specific tasks by convention
  26 available for general use, but constrained by convention

## Slide 22: MIPS Instruction Formats
All MIPS instructions fit into a single 32-bit word
Every instruction includes various “fields”:
  a 6-bit operation or “OPCODE”
    specifies which operation to execute (fewer than 64)
  up to three 5-bit OPERAND fields
    each specifies a register (one of 32) as source/destination
  embedded constants
    also called “literal” or “immediate”
    16-bits, 5-bits or 26-bits long (you will see in a minute, why)
    sometimes treated as signed values, sometimes unsigned
There are three basic instruction formats:
R-type, 3 register operands (2 sources, destination)
I-type, 2 register operands, 16-bit constant
OP
rs
rt
rd
OP
rs
rt
16-bit constant
func
shamt
J-type, no register operands, 26-bit constant
OP
26-bit constant