## Slide 1: ISA (Instruction Set Architecture) Part II
Ergun Simsek
CMSC 411 | Lecture 6 | Fall 2022

## Slide 2
Brief of last class
  von Neumann model of a computer
  Introduction to ISA (Instruction Set Architecture)
Today
  MIPS Instructions
  How to use the MIPS Reference Card (Green Card)

## Slide 3: The Stored-Program Computer
The von Neumann model:
  Instructions and Data stored in a common memory (“main memory”)
  Sequential semantics: All instructions execute sequentially (or at least appear sequential to the programmer)
Key idea: Memory holds not only data, but coded instructions that make up a program.
Central
Processing Unit
Main Memory
instruction
instruction
instruction
data
data
data
CPU fetches and executes instructions from memory ...
  The CPU is a hardware interpreter
  Program IS simply data for this interpreter
  Main memory: Single expandable resource pool - constrains both data and program size - don’t need to make separate decisions of how large of a program or data memory to buy

## Slide 4: Register File
11111
00000
10110

## Slide 5: Recap: MIPS Instruction Formats
All MIPS instructions fit into a single 32-bit word
Every instruction includes various “fields”:
  a 6-bit operation or “OPCODE”
    specifies which operation to execute (fewer than 64)
  We either have 3 or 2 5-bit OPERAND fields which specify a register (one of 32) as source/destination
  If we don’t have three operand fields, then it means we have an “immediate”
    sometimes treated as signed values, sometimes unsigned
NO FUNCT
CODE FOR
I- and J- insts.

## Slide 6: MIPS Reference Data (Green Card)
Ins | Opcode | Funct | Type
add |  |  | 
addi |  |  | 
000000 100000 R
001000 I
Const is 16-bit two's comp.
sign-extended to 32 bits
addiu
Const is 16-bit two's comp.
sign-extended to 32 bits
No overflow trap.
Get familiar with bit numbers!

## Slide 7: MIPS ALU Operations
Sample coded operation: ADD instruction
add $10, $11, $9
0
0
0
0
0
0
0
1
0
1
1
0
1
0
0
1
0
1
0
1
0
1
0
0
0
0
0
0
0
0
0
0
op = 0x00 dictating an ALU function
rs = 11 Reg[11]
source
rd = 10 Reg[10]
destination
rt = 9 Reg[9]
source
unused fields are set to ‘0’
func = 0x20 dictating an add
R-type:

## Slide 8: MIPS Since Cycle Datapath
0
0
0
0
0
0
0
1
0
1
1
0
1
0
0
1
0
1
0
1
0
1
0
0
0
0
0
0
0
0
0
0
add rd, rs, rt
add $10, $11, $9
Bits [31-26]
[5-0]
[10-6]
[15-11]
[20-16]
[25-21]
[15-0]

## Slide 9: Function Code Examples
Instruction Function
add rd, rs, rt 100000
addu rd, rs, rt 100001
and rd, rs, rt 100100
break 001101
div rs, rt 011010
divu rs, rt 011011
jalr rd, rs 001001
jr rs 001000
mfhi rd 010000
mflo rd 010010
mthi rs 010001
mtlo rs 010011
mult rs, rt 011000
multu rs, rt 011001
nor rd, rs, rt 100111
or rd, rs, rt 100101
sll rd, rt, sa 000000
sllv rd, rt, rs 000100
slt rd, rs, rt 101010
sltu rd, rs, rt 101011
sra rd, rt, sa 000011
srav rd, rt, rs 000111
srl rd, rt, sa 000010
Instruction Function
srlv rd, rt, rs 000110
sub rd, rs, rt 100010
subu rd, rs, rt 100011
syscall 001100
xor rd, rs, rt 100110

## Slide 10: Shift operations
Shifting is a common operation
  applied to groups of bits
  used for alignment
  used for “short cut” arithmetic operations
    X << 1 is often the same as 2*X
    X >> 1 can be the same as X/2
For example:
  X = 2010 = 000101002
  Left Shift:
    (X << 1) = 001010002 = 4010
  Right Shift:
    (X >> 1) = 000010102 = 1010
  Signed Right Shift requires inserting MSB, which is not always 0
    (-X >>> 1) = (111011002 >>> 1) =
111101102 = -1010

## Slide 11: MIPS Shift Operations
Sample coded operation: SHIFT LOGICAL LEFT instruction
Assembly: sll $2, $2, 4
sll rd, rt, shamt:
“Shift the contents of rt to the left by shamt; store the result in rd”
Reg[rd] = Reg[rt] << shamt
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
1
0
0
0
0
0
0
0
0
0
1
0
0
op = 0x00 dictating an ALU function
unused set to
‘0’
rd = 2 Reg[2]
destination
rt = 2 Reg[2]
source
shamt = 4 dictates a shift of 4-bits
func = 0x00 dictating an sll
R-type:

## Slide 12: MIPS Shift Operations
Sample coded operation: SLLV (SLL Variable)
0
0
0
0
0
0
0
1
0
0
0
0
0
0
1
0
0
0
0
1
0
0
0
0
1
0
0
0
0
0
0
0
op = 0x00 dictating an ALU function
shift
amount
in rs
rd = 2 Reg[2]
destination
rt = 2 Reg[2]
source
unused set to ‘0’
func = 0x04 dictating an sllv
Assembly: sllv $2, $2, $4
sllv rd, rt, rs:
“Shift the contents of rt left by the contents of rs; store the result in rd”
Reg[rd] = Reg[rt] << Reg[rs]
R-type:
Different flavor:
Shift amount is not in instruction, but in a register

## Slide 13: MIPS ALU Operations with Immediate
addi instruction: adds register contents, signed-constant:
Symbolic version: addi $9, $11, -3
“Add the contents of rs to const; store result in rt”
OP = 0x08, dictating addi
rs = 11, Reg[11] source
rt = 9, Reg[9] destination
Reg[rt] = Reg[rs] + sxt(imm)
arithmetic: addi, addiu
compare: slti, sltiu
logical: andi, ori, xori, lui
Similar instructions for other ALU operations:
constant field, indicating -3 as second operand
(sign-extended!)
addi rt, rs, imm:
0
0
1
0
0
0
0
1
0
1
1
0
1
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
1
Immediate values are sign-extended for arithmetic and compare operations, but not for logical operations.
I-type:
    FACT: In a C compiler (gcc), 52% of ALU operations use a constant!

## Slide 14: Working with Constants
  Examples
    add 2000 to register $5
    addi $5, $5, 2000
    subtract 60 from register $5
    addi $5, $5, -60
      … no subi instruction!
    put the number 1234 in $10
    addi $10, $0, 1234
    logically AND $5 with 0x8723 and put the result in $7
    andi $7, $5, 0x8723
  But…
    these constants are limited to 16 bits only!
      Range is [-32768…32767] if signed, or [0…65535] if unsigned
215 = 32768

## Slide 15: Beware ADDIU: “add immediate unsigned”
addiu: supposedly “add immediate unsigned”
BUT IS A MISNOMER! Actually sign-extends the immediate.
The difference between addi & addiu is that addiu doesn’t check for overflows
Symbolic version: addiu $9, $11, -3
“Add the contents of rs to const; store result in rt”
OP = 0x09, dictating addiu
rs = 11, Reg[11] source
rt = 9, Reg[9] destination
Reg[rt] = Reg[rs] + sign-ext(imm)
constant field, indicating -3 as second operand
(sign-extended!)
addiu rt, rs, imm:
0
0
1
0
0
1
0
1
0
1
1
0
1
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
1
I-type:

## Slide 16: ORI: Unsigned Constants
ori instruction: bitwise OR’s register to unsigned-constant:
Symbolic version: ori $9, $11, 65533
“OR the contents of rs to const; store result in rt”
OP = 0x0d, dictating ori
rs = 11, Reg[11] source
rt = 9, Reg[9] destination
Reg[rt] = Reg[rs] | zero-ext(imm)
Also: All logical operations are always “unsigned”, so always zero-extended:
ori, andi, xori
constant field, indicating 65533 as second operand
(zero-extended!)
ori rt, rs, imm:
0
0
1
1
0
1
0
1
0
1
1
0
1
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
1
I-type:
The imm is 0-padded into a 32-bit unsigned (+ve) number:
00000000000000001111111111111101

## Slide 17: How About Larger Constants?
Problem: How do we work with bigger constants?
  Example: Put the 32-bit value 0x5678ABCD in $5
  CLASS: How will you do it?
One Solution:
  put the upper half (0x5678) into $5
  then shift it left by 16 positions (0x5678 0000)
  now “add” the lower half to it (0x5678 0000 + 0xABCD)
  addi $5, $0, 0x5678
  sll $5, $5, 16
  addi $5, $5, 0xABCD
One minor problem with this:
  2nd addi can mess up by treating the constants are signed
  use ori instead

## Slide 18: How About Larger Constants?
Observation: This sequence is very common!
  so, a special instruction was introduced to make it shorter
  the first two (addi + sll) combo is performed by
  lui
  “load upper immediate”
    puts the 16-bit immediate into the upper half of a register
  Example: Put the 32-bit value 0x5678ABCD in $5
  lui $5, 0x5678
  ori $5, $5, 0xABCD
0101011001111000
0000000000000000
0000000000000000
1010101111001101
0101011001111000
1010101111001101
Reminder: In MIPS, Logical Immediate instructions (ANDI, ORI, XORI) do not sign-extend their constant operand

## Slide 19: MIPS Operations

## Slide 20: Exercise
Compute the following expression with MIPS Assembly
  f = (g + h) – (i + j)
  where variables f, g, h, i, and j are assigned to registers $16, $17, $18, $19, and $20 respectively
  add $8,$17,$18
  add $9,$19,$20
  sub $16,$8,$9