## Slide 1: ISA (Instruction Set Architecture) Part III
Ergun Simsek
CMSC 411 | Lecture 7 | Fall 2022

## Slide 2
Last class
  MIPS Instructions
  How to use the MIPS Reference Card (Green Card)
Today
  MIPS Instructions: Branching, Multiplication, Division, Logical
  Accessing Memory
  Addressing Modes

## Slide 3: MIPS Branch Instructions
if (REG[RS] != REG[RT])
{ PC = PC + 4 + 4*offset; }
bne rs, rt, label # Branch if not equal
if (REG[RS] == REG[RT])
{ PC = PC + 4 + 4*offset; }
beq rs, rt, label # Branch if equal
NB: Branch targets are specified relative to the next instruction (which would be fetched by default). The assembler hides the calculation of these offset values from the user, by allowing them to specify a target address (usually a label) and it does the job of computing the offset’s value. The size of the constant field (16-bits) limits the range of branches.
OPCODE
rs
rt
16-bit signed constant
MIPS branch instructions provide a way of conditionally changing the PC to some nearby location...
I-type:
Notice on memory references offsets are multiplied by 4, so that branch targets are restricted to word boundaries.

## Slide 4: MIPS Jumps
The range of MIPS branch instructions is limited to approximately  32K instructions ( 128K bytes) from the branch instruction.
To branch farther: an unconditional jump instruction is used.
Instructions:
  j label # jump to label (PC = { PC[31-28], CONST[25:0]*4) }
  lower 28 bits are the const * 4
  upper 4 bits are from the current PC value
  “ { } ” here means concatenate them together
  jal label # jump to label and store PC+4 in $31
  jr $t0 # jump to address specified by register’s contents
  jalr $t0, $ra # jump to address specified by first register’s contents and store PC+4 in second register
Formats:
J-type: used for j
OP = 2
26-bit constant
J-type: used for jal
OP = 3
26-bit constant
R-type, used for jr
OP = 0
rs
func = 8
0
0
0
R-type, used for jalr
OP = 0
rs
func = 9
0
0
rd
Notes: The uses of jal and jr are tied together.
These instructions may be used for subroutine or procedure calls, to provide a convenient entry to/exit from utility software.
  – jal sub – the next instruction executed is in a different code segment, starting at memory location “sub.” The processor stores the address of the instruction following the jal instruction ([PC]+4) in $ra.
  – At the conclusion of the called routine (starting at label “sub”), the last instruction is jr $ra. This returns the program to its primary flow at the instruction that followed the original jal.

## Slide 5: Multiply and Divide
Slightly more complicated than add/subtract
  multiply: product is twice as long!
    if A, B are 32-bit long, A * B is how many bits?
  divide: dividing integer A by B gives two results!
    quotient and remainder
Solution: two new special-purpose registers
  “Hi” and “Lo”

## Slide 6: Multiply: MULT instruction
  mult rs, rt
  Meaning: multiply contents of registers $rs and $rt, and store the (64-bit result) in the pair of special registers {hi, lo}
    hi:lo = $rs * $rt
  upper 32 bits go into hi, lower 32 bits go into lo
To access result, use two new instructions
  mfhi: move from hi, i.e., move the 32-bit half result from hi to $rd
    mfhi rd
  mflo: move from lo, i.e., move the 32-bit half result from lo to $rd
    mflo rd
mult $a0, $a1
mfhi $a2 # 32 most significant bits of multiplication to $a2
mflo $v0 # 32 least significant bits of multiplication to $v0

## Slide 7: Divide: DIV instruction
  div rs, rt
  Meaning: divide contents of register $rs by $rt, and store the quotient in lo, and remainder in hi
    lo = $rs / $rt
    hi = $rs % $rt
To access result, use mfhi and mflo
NOTE: There are also unsigned versions
  multu
  divu

## Slide 8: Comparison: slt, slti
slt = set-if-less-than
  slt rd, rs, rt
  $rd = ($rs < $rt) // “1” if true and “0” if false
slti = set-if-less-than-immediate
  slti rt, rs, imm
  $rt = ($rs < sign-ext(imm))
also other flavors
  sltu
  sltiu

## Slide 9: Logical Instructions
Boolean operations: bitwise on all 32 bits
  operations: AND, OR, NOR, XOR
  instructions:
    and, andi
    or, ori
    nor // Note: There is no nori
    xor, xori
Examples:
  and $1, $2, $3
  $1 = $2 & $3
  xori $1, $2, 0xFF12
  $1 = $2 ^ 0x0000FF12
  See all in textbook!

## Slide 10: Accessing Memory
MIPS is a “load-store” architecture
  all operands for ALU instructions are in registers or immediate
  cannot directly add values residing in memory
    must first bring values into registers from memory (called LOAD)
    must store result of computation back into memory (called STORE)
Control Unit
Data
Path
registers
MEMORY
control
status
instructions
data
address
address

## Slide 11: MIPS Load Instruction
Load instruction is I-type
  Does the following:
    takes the value stored in register $rs
    adds to it the immediate value (signed)
    this is the address where memory is looked up
    value found at this address in memory is brought in and stored in register $rt
lw rt, imm(rs)
Meaning: Reg[rt]= Mem[Reg[rs] + sign-ext(imm)]
Abbreviation: lw rt,imm for lw rt, imm($0)
OP
rs
rt
16-bit signed constant
I-type:

## Slide 12: MIPS Store Instruction
Store instruction is also I-type
  Does the following:
    takes the value stored in register $rs
    adds to it the immediate value (signed)
    this is the address where memory is accessed
    reads the value from register $rt and writes it into the memory at the address computed
sw rt, imm(rs)
Meaning: Mem[Reg[rs] + sign-ext(imm)] = Reg[rt]
Abbreviation: sw rt,imm for sw rt, imm($0)
OP
rs
rt
16-bit signed constant
I-type:

## Slide 13: MIPS Memory Addresses
lw and sw read whole 32-bit words
  so, addresses computed must be multiples of 4
    Reg[rs] + sign-ext(imm) must end in “00” in binary
  otherwise: runtime exception
There are also byte-sized flavors of these instructions
  lb (load byte)
    Loads the byte from memory into the low order eight bits of the register. These are bits 0-7 of the register.
    Then it copies bit 7 to bits 8-31 of the register (all bits to the left of bit 7).
  sb (store byte)
  lb/sb addresses do not have to be multiples of 4

## Slide 14: Example
Memory at 0x10000007 contains the byte 0xA4
Register $8 contains 0x10000000
What is put in register $10 when the following instruction is executed:
lb $10,7($8)
What is put in register $12 when the following instruction is executed:
lbu $12,7($8)
$10 = 0xFFFFFFA4
Bit 7 of 0xA4 is 1, so lb extends that bit to all high order three bytes of $10.
$12 = 0x000000A4
lbu zero-extends the byte from memory.

## Slide 15: Storage Conventions
Data stored in memory
  addresses in memory are assigned at compile time
  data values must be “loaded” into registers first
  operations done on registers
  result stored in memory
Example
  assume compiler has assigned these memory addresses
1000:
1004:
1008:
1010:
100C:
n
r
x
y
int x, y;
y = x + 37;
lw $t0, 0x1008($0)
addi $t0, $t0, 37
sw $t0, 0x100C($0)
translates
to:
Compilation approach:
LOAD, COMPUTE, STORE
choice of $t0 is arbitrary

## Slide 16: Some Notes About PC
Both data and text (instructions) are stored in memory.
However, these two quantities are stored in different areas of memory, and accessed by different data pathways.
The MIPS computer can address 4 Gbyte of memory, from address 0x0000 0000 to 0xffff ffff.
User memory is limited to locations below 0x7fff ffff.
Text (program) storage always starts at 0x0040 0000.
Data storage generally* starts at 0x1001 0000.
Data and instructions enter the CPU via different pathways.
  Data must enter via the register block.
  Instructions proceed directly to the instruction decoder in the CPU
Memory
* Different implementations use slightly different address

## Slide 17: Addressing Modes
Today’s modern CPUs can have very complex addressing modes, but MIPS is not one of them.
In MIPS, there are three modes
Absolute (Direct): lw $8, 0x1000($0)
  Value = Mem[constant]
  Use: accessing static data
Register-Indirect: lw $8, 0($9)
  Value = Mem[Reg[x]]
  Use: pointer accesses
Displacement: lw $8, 16($9)
  Value = Mem[Reg[x] + constant]
  Use: access to local variables
Scaled:
  Value = Mem[Reg[x] + c + d*Reg[y]]
  Use: array accesses (base+index)
Do you want to see a complex one?

## Slide 18: Absolute (Direct) Addressing
What we want:
  Contents of a specific memory location, i.e. at a given address
Example:
Warning
  Sometimes generates a two-instruction sequence
    If the address for x chosen by the programmer/compiler/assembler is too large to fit within the 16-bit immediate field
“C”
int x = 10;
main() {
x = x + 1;
}
“MIPS Assembly”
.data
x: .word 10
.text
main:
lw $2,x($0)
addi $2,$2,1
sw $2,x($0)
lui $1,xhighbits
lw $2,xlowbits($1)
Allocates space for a single integer (4-bytes) and initializes its value to 10
‘x’ here means address of x
lui $1,0x1234
lw $2,0x5678($1)
e.g., if x is at address 0x12345678

## Slide 19: Absolute (Direct) Addressing: More detail
“C”
int x = 10;
main() {
x = x + 1;
}
“MIPS Assembly”
.data
x: .word 10
.text
main:
lw $2,x($0)
addi $2,$2,1
sw $2,x($0)
“After Compilation”
.data 0x0100
x: .word 10
.text
main:
lw $2,0x100($0)
addi $2,$2,1
sw $2,0x100($0)
Assembler replaces “x” by its address
  e.g., here the data part of the code (.data) starts at 0x100
  x is the first variable, so starts at 0x100
    this mode works in MIPS only if the address fits in 16 bits

## Slide 20: What does this code do?
“C”
int x = 10;
main() {
int *y = &x;
*y = 2;
}
x is the address of the value, which is 10
&x is the address of the pointer that contains the address of the value
*y is the value

## Slide 21: Indirect Addressing
What we want:
  The contents at a memory address held in a register
Examples
Warning
  You must make sure that the register contains a valid address (double, word, or short aligned as required)
“C”
int x = 10;
main() {
int *y = &x;
*y = 2;
}
“MIPS Assembly”
.data
x: .word 10
.text
main:
la $2,x
addi $3,$0,2
sw $3,0($2)
lui $2,xhighbits
ori $2,$2,xlowbits
la: load address
“la” is not a real instruction,
It’s a convenient pseudoinstruction that constructs a constant via either a 1 instruction or 2 instruction sequence
ori $2,$0,x
$2 performs the role of y, i.e., it is a pointer to x
Notes: remember that when do “ori” x with 32-bit 0, we basically do zero-extension

## Slide 22: Note on la pseudoinstruction
la is a pseudoinstruction: la $r, x
  stands for “load the address of” variable x into register r
  not an actual MIPS instruction
  but broken down by the assembler into actual instructions
    if address of x is small (fits within 16 bits), then a single ori
      one could also use a single addiu
    if address of x is larger, use the lui + ori combo
“MIPS Assembly”
.data
x: .word 10
.text
.global main
main:
la $2,x
addi $3,$0,2
sw $3,0($2)
lui $2,0x8000
ori $2,$2,0x0010
ori $2,$0,0x100
0x0100
0x80000010
if
if

## Slide 23: Displacement Addressing
What we want:
  contents of a memory location at an offset relative to a register
    the address that is the sum of a constant and a register value
Example:
Remember:
  Must multiply (shift) the “index” to be properly aligned
“C”
int a[5];
main() {
int i = 3;
a[i] = 2;
}
“MIPS Assembly”
.data
a: .space 20
.text
main:
addi $2,$0,3 // i in $2
addi $3,$0,2
sll $1,$2,2 // i*4 in $1
sw $3,a($1)
Allocates space for a 5 uninitialized integers (20-bytes)
a[4] | a[3] | a[2] | a[1] | a[0]
19-16 | 15-12 | 11-8 | 7-4 | 3-0

## Slide 24: Displacement Addressing: 2nd example
What we want:
  The contents of a memory location at an offset relative to a register
Example:
Note:
  offsets to the various fields within a structure are constants known to the assembler/compiler
“C”
struct p {
int x, y; }
main() {
p.x = 13;
p.y = 12;
}
“MIPS Assembly”
.data
p: .space 8
.text
main:
la $1,p
addi $2,$0,13
sw $2,0($1)
addi $2,$0,12
sw $2,4($1)
Allocates space for 2 uninitialized integers (8-bytes)

## Slide 25: Practice Problem: Store offsets
The variable A is stored at memory address 24. We want to change its value to 512. Which of the following combinations of R5, R6, and the constant X will accomplish this with the instruction sw R6, X(R5)?
R6=512, X=0, R5=24
R6=512, X=24, R5=0
R6=24, X=512, R5=0
R6=24, X=0, R5=512
Notes: Concepts: address calculation, data/addresses

## Slide 26: Now we can do a real program: Factorial...
n: .word 11 # suppose mem loc 0x1000
ans: .word 0 # suppose mem loc 0x1004
...
addi $t0, $0, 1 # t0 = 1
lw $t1, 0x1000($0) # t1 = n
loop: beq $t1, $0, done # while (t1 != 0)
mult $t0, $t1 # hi:lo = t0 * t1
mflo $t0 # t0 = t0 * t1
addi $t1, $t1, -1 # t1 = t1 - 1
j loop # Always loop back
done: sw $t0, 0x1004($0) # ans = r1
int n=11;
int ans=0;
int r1, r2;
r1 = 1;
r2 = n;
while (r2 != 0) {
r1 = r1 * r2;
r2 = r2 – 1; }
ans = r1;
Synopsis (in C):
  Input in n, output in ans
  r1, r2 used for temporaries
  assume n is small
MIPS code, in assembly language:

## Slide 27: Summary - 1

## Slide 28: Summary - 2

## Slide 29: MIPS Instruction Decoding Ring
Top table summarizes opcodes
Bottom table summarizes func field if opcode is 000000
OP | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
000 | func |  | j | jal | beq | bne |  | 
001 | addi | addiu | slti | sltiu | andi | ori | xori | lui
010 |  |  |  |  |  |  |  | 
011 |  |  |  |  |  |  |  | 
100 |  |  |  | lw |  |  |  | 
101 |  |  |  | sw |  |  |  | 
110 |  |  |  |  |  |  |  | 
111 |  |  |  |  |  |  |  | 
func | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
000 | sll |  | srl | sra | sllv |  | srlv | srav
001 | jr | jalr |  |  |  |  |  | 
010 |  |  |  |  |  |  |  | 
011 | mult | multu | div | divu |  |  |  | 
100 | add | addu | sub | subu | and | or | xor | nor
101 |  |  | slt | sltu |  |  |  | 
110 |  |  |  |  |  |  |  | 
111 |  |  |  |  |  |  |  | 

## Slide 30: Summary
We will use a subset of MIPS instruction set in this class
  Sometimes called “miniMIPS”
  All instructions are 32-bit
  3 basic instruction formats
    R-type - Mostly 2 source and 1 destination register
    I-type - 1-source, a small (16-bit) constant, and a destination register
    J-type - A large (26-bit) constant used for jumps
  Load/Store architecture
  31 general purpose registers, one hardwired to 0, and, by convention, several are used for specific purposes.
ISA design requires tradeoffs, usually based on
  History, Art, Engineering
  Benchmark results